## Slide 1: Jennifer Uhle Director of Reactor Safety Programs 4/21/17
NRC Licensing of Advanced Reactors

## Slide 2: Contents
A quick summary of the licensing process and NRC plans to be ready to license advanced reactors.
Part 50 and Part 52
Status of Small Modular Reactors
NRC experience with non-LWRs
NRC Vision and Strategy
NRC Readiness Advanced Reactors
Conclusions

## Slide 3: Licensing under 10 CFR Parts 50 and 52
Advanced Reactors are expected to be licensed under Part 52 which leads to standard design certification.
Part 50
2 Steps by the utility
  1 - Construction Permit
  2 - Operating License
Pros
  Can start construction early
  Design risk can be shared
Cons
  Construction risk is high
  Each plant is one-of-a-kind
Part 52
1 Step for each partner
  Vendor - Design Certification
  Utility – Combined License
Pros
  Certified Design is a rule
  Licensing scope is reduced
Cons
  Construction once COL is issued

## Slide 4: Options in the Licensing Process
The regulatory process is flexible.
Staged Licensing under
Part 52 Subpart E
CDA
CDA = Conceptual Design Assessment
Design Certification
Ideal for venture capital funded
programs
Construction while
completing the design
with Part 50
Needs a utility and a
site, and is the fastest
way to operation
However, no design certification is granted
Licensing a prototype
Under 50.43(e)(2)
Uncertainty managed
by additional defense
in depth
Available under Part 50
and Part 52

## Slide 5: Prototype Plants
Prototype is a first-of-a-kind plant and can be full size.
Additional safety features will be required to protect public health and safety.
Tests can be run and used in further licensing.
Available using Part 50 or Part 52.
NRC is developing guidance for this option.
Notes: In any one design there may be particular phenomena that are of higher uncertainty. This could definitely kick you out of the fast lane. However, the regulations allow for uncertainty in a phenomenon or feature to be managed by adding additional safety features to the plant. Although this has not been exercised as far as I know, a prototype reactor can be built and operated. It is similar to a first-of-a-kind plant in all features and size, but may include additional safety features to protect the public and the plant staff from the possible consequences of accidents during the testing period. Tests can be run in the plant to supplement the knowledge base which would then allow the additional features to no longer be required, if appropriate. This is available for Part 50 and Part 52. The NRC is developing guidance for this option.
DETAILS
50.2 Defintitions
Prototype plant means a nuclear reactor that is used to test design features, such as the testing required under § 50.43(e). The prototype plant is similar to a first-of-a-kind or standard plant design in all features and size, but may include additional safety features to protect the public and the plant staff from the possible consequences of accidents during the testing period.
50.43 Additional standards and provisions affecting class 103 licenses and certifications for commercial power.
(e) Applications for a design certification, combined license, manufacturing license, or operating license that propose nuclear reactor designs which differ significantly from light-water reactor designs that were licensed before 1997, or use simplified, inherent, passive, or other innovative means to accomplish their safety functions, will be approved only if:
1) (i) The performance of each safety feature of the design has been demonstrated through either analysis, appropriate test programs, experience, or a combination thereof;
(ii) Interdependent effects among the safety features of the design are acceptable, as demonstrated by analysis, appropriate test programs, experience, or a combination thereof; and
(iii) Sufficient data exist on the safety features of the design to assess the analytical tools used for safety analyses over a sufficient range of normal operating conditions, transient conditions, and specified accident sequences, including equilibrium core conditions; or
(2)There has been acceptable testing of a prototype plant over a sufficient range of normal operating conditions, transient conditions, and specified accident sequences, including equilibrium core conditions. If a prototype plant is used to comply with the testing requirements, then the NRC may impose additional requirements on siting, safety features, or operational conditions for the prototype plant to protect the public and the plant staff from the possible consequences of accidents during the testing period.

## Slide 6: NuScale Small Modular Reactor Design
  Passive safety
  light-water integral pressurized water reactor (iPWR)
  Internal helical steam generator
  and pressurizer
  Electric output of 50 MWe
  Up to 12 modules
NRC design review is underway.
Accidents are designed out!

## Slide 7: NuScale Construction and Siting
Factory built
Modules delivered by barge, truck, or train
Remote siting is facilitated.

## Slide 8: NRC History with Advanced Reactors
The NRC could review and license a non-LWR today.
Between 1951 – 2010, the AEC/NRC reviewed 20 non-LWRs
  Liquid metal
    Fermi 1 -- CP in 1956, OL in 1963, shutdown in 1972
  HTGR
    Fort St. Vrain -- CP in 1968, OL in 1973, shutdown in 1989
    Peach Bottom -- , CP in 1961, OL in 1966, shutdown in 1974
  Thorium fuel cycle in Shippingport, 3rd core
  Construction Permit for Clinch River breeder reactor in 1983
  Preliminary SERs
    PRISM (1990’s), SAFR (1991), mHTGR (1995), ACR-700 (2004), PBMR (2010)
The NRC needs to be efficient, effective and flexible
  The NRC issued a CP for SHINE in 2016 (Moly-99 medical isotope facility)

## Slide 9: NRC Vision and Strategy
Non-LWR Mission Readiness Roadmap
STRATEGIC OBJECTIVES & STRATEGIES
MISSION
VISION
STRATEGIC GOAL FOR NON-LWRs
IMPLEMENTATION ACTION PLANS & TASK EXECUTION
DOE non-LWR Vision & Goals Alignment Point
- Near-Term (0-5 yr)
- Mid-Term (5-10 yr)
- Long-Term (10+ yr)

## Slide 10: NRC Readiness
“Readiness” means that all the elements that NRC needs to conduct its mission are in place and optimized.
  People (staff training)
  Processes (procedures and guidance)
  Tools (computer models)
  Policies (emergency preparedness requirements)
  Decision Criteria (design-specific review standards)
  Transparency and Clarity of Requirements
  Communication (workshops)

## Slide 11: Conclusions
Idaho National Laboratory plays a key role in the Nation’s deployment of advanced reactors.
Advanced reactor expertise
Experimental facilities
Computer system analysis tools
Fuel qualification facilities
Policy issue resolution
Technical training

## Slide 12: QUESTIONS?
For More Information Visit
www.jensenhughes.com
CONTACT
Jennifer Uhle
JUhle@jensenjughes.com
202-604-2572